## Slide 1
路由与交换技术
第 13 讲

## Slide 2: 内容回顾
网络安全技术的基本概念
ACL的概述、应用和分类
ACL的工作流程
ACL的配置任务

## Slide 3: 网络地址转换（NAT）

## Slide 4
网络迅速发展， IPv4地址不敷使用
IPv4地址分配不均
私有地址用户需要访问Internet
NAT提供私有地址到公有地址的转换
引入

## Slide 5
NAT概述
Basic NAT
NAPT
Easy IP
NAT Server
NAT ALG
NAT的信息显示和调试
目录

## Slide 6: 公有地址和私有地址
私有地址范围：
10.0.0.0 - 10.255.255.255
172.16.0.0 - 172.31.255.255
192.168.0.0 - 192.168.255.255
公司A
10.0.0.0/8
公司B
10.0.0.0/8
公司C
10.0.0.0/8
Internet
任何组织都可以任意使用私有地址空间
私有地址在Internet上无法路由
如果采用私有地址的网络需要访问Internet，必须在出口处部署NAT设备

## Slide 7: NAT组网和常用术语
私网
公网
10.0.0.1
HostA
10.0.0.254/24
198.76.28.1/24
HostB
10.0.0.2
Internet
Server
198.76.29.4/24
地址池
198.76.28.11
198.76.28.12
……
198.76.28.20
Internet
NAT设备

## Slide 8: Basic NAT
10.0.0.1
HostA
RTA
10.0.0.254/24
198.76.28.1/24
HostB
10.0.0.2
Internet
Server
198.76.29.4/24
地址池
（198.76.28.11～20）
Internet
S=10.0.0.1
D=198.76.29.4
S=198.76.28.11
D=198.76.29.4
S=198.76.29.4
D=198.76.28.11
S=198.76.29.4
D=10.0.0.1
10.0.0.2
198.76.28.12
NAT table
Inside Address
10.0.0.1
198.76.28.11
Global Address
1
2
3
4
6
5

## Slide 9: 配置Basic NAT
配置ACL
  用于判断哪些数据包的地址应被转换
  被ACL允许（permit）的报文将被进行NAT转换，被拒绝（deny）的报文将不会被转换
配置地址池
  nat address-group group-number
  address start-address end-address
配置地址转换
  nat outbound acl-number address-group group-number no-pat

## Slide 10: Basic NAT配置示例
10.0.0.1
RTA
10.0.0.254/24
198.76.28.1/24
10.0.0.2
Internet
Server
Internet
[RTA]acl number 2000
[RTA-acl-basic-2000]rule 0 permit source 10.0.0.0 0.0.0.255
[RTA]nat address-group 1
[RTA-address-group-1]address 198.76.28.11 198.76.28.20
[RTA]interface GigabitEthernet 0/1
[RTA-GigabitEthernet0/1]nat outbound 2000 address-group 1 no-pat
GE0/1
198.76.29.4/24
HostA
HostB
地址池
（198.76.28.11～20）

## Slide 11: NAPT
NAT table
S=10.0.0.1 P=1024
D=198.76.29.4 P=80
S=198.76.28.11 P=2001
D=198.76.29.4 P=80
S=198.76.29.4 P=80
D=198.76.28.11 P=2001
S=198.76.29.4 P=80
D=10.0.0.1 P=1024
10.0.0.2:1024
198.76.28.11:3001
Inside Address
Port
10.0.0.1:1024
198.76.28.11:2001
Global Address
Port
10.0.0.1
HostA
RTA
10.0.0.254/24
198.76.28.1/24
HostB
10.0.0.2
Internet
Server
198.76.29.4/24
地址池
（198.76.28.11～20）
Internet
1
2
3
4
6
5

## Slide 12: 配置NAPT
配置ACL
  用于判断哪些数据包的地址应被转换
  被ACL允许（permit）的报文将被进行NAT转换，被拒绝（deny）的报文将不会被转换
配置地址池
  nat address-group group-number
  address start-address end-address
配置地址转换
  nat outbound acl-number address-group group-number

## Slide 13: NAPT配置举例
10.0.0.1
RTA
10.0.0.254/24
198.76.28.1/24
10.0.0.2
Internet
Server
地址池
（198.76.28.11）
Internet
[RTA]acl number 2000
[RTA-acl-basic-2000]rule 0 permit source 10.0.0.0 0.0.0.255
[RTA]nat address-group 1
[RTA-address-group-1]address 198.76.28.11 198.76.28.11
[RTA]interface GigabitEthernet 0/1
[RTA-GigabitEthernet0/1]nat outbound 2000 address-group 1
GE0/1
HostB
HostA
198.76.29.4/24

## Slide 14: Easy IP
NAT设备直接使用出接口的IP地址作为转换后的源地址
不用预先配置地址池
工作原理与普通NAPT相同，是NAPT的一种特例
适用于拨号接入Internet或动态获得IP地址的场合

## Slide 15: 配置Easy IP
配置ACL
  用于判断哪些数据包的地址应被转换
  被ACL允许（permit）的报文将被进行NAT转换，被拒绝（deny）的报文将不会被转换
配置地址转换
  nat outbound acl-number

## Slide 16: Easy IP配置举例
10.0.0.1
RTA
10.0.0.254/24
198.76.28.1/24
10.0.0.2
Internet
Server
Internet
[RTA]acl number 2000
[RTA-acl-basic-2000]rule 0 permit source 10.0.0.0 0.0.0.255
[RTA]interface GigabitEthernet 0/1
[RTA-GigabitEthernet0/1]nat outbound 2000
GE0/1
198.76.29.4/24
HostA
HostB

## Slide 17: NAT Server
NAT Server
S=10.0.0.1 P=8080
D=198.76.29.4 P=1033
S=198.76.28.11 P=80
D=198.76.29.4 P=1033
S=198.76.29.4 P=1033
D=198.76.28.11 P=80
S=198.76.29.4 P=1033
D=10.0.0.1 P=8080
Inside Address
Port
10.0.0.1:8080
198.76.28.11:80
Global Address
Port
10.0.0.1
HostA
RTA
10.0.0.254/24
198.76.28.1/24
HostB
10.0.0.2
Internet
HostC
198.76.29.4/24
Internet
4
5
6
1
3
2
E0/0

## Slide 18: 配置NAT Server
NAT Server配置命令
  nat server protocol pro-type global global-addr [ global-port ] inside host-addr [ host-port ]

## Slide 19: NAT Server配置举例
10.0.0.1
RTA
10.0.0.254/24
198.76.28.1/24
10.0.0.2
Internet
HostC
Internet
[RTA]interface GigabitEthernet 0/1
[RTA-GigabitEthernet0/1]nat server protocol tcp global 198.76.28.11 telnet inside 10.0.0.1 telnet
GE0/1
Telnet Server
HostB
198.76.29.4/24

## Slide 20: NAT ALG
FTP Control 通道
FTP Data 通道
NAT table
S=10.0.0.1 P=1024
D=198.76.29.4 P=21
S=198.76.28.11 P=2001
D=198.76.29.4 P=21
S=198.76.29.4 P=21
D=198.76.28.11 P=2002
S=198.76.29.4 P=21
D=10.0.0.1 P=5001
10.0.0.1:5001
198.76.28.11:2002
Inside Address
Port
10.0.0.1:1024
198.76.28.11:2001
Global Address
Port
10.0.0.1
HostA
RTA
10.0.0.254/24
198.76.28.1/24
HostB
10.0.0.2
Internet
FTP Server
198.76.29.4/24
地址池
（198.76.28.11～20）
Internet
1
2
3
4
6
5
“S=10.0.0.1 P=5001”
“S=198.76.28.11 P=2002”

## Slide 21: NAT的信息显示和调试
显示地址转换信息
调试地址转换过程
清除地址转换连接
  <H3C> display nat { address-group group-number | all | outbound port-block-group | server | statistics | session }
  <H3C> debugging nat { alg | config | event | packet acl number }
  <H3C> reset nat session

## Slide 22
NAT可以有限缓解IPv4地址短缺，并提高安全性
Basic NAT实现私网地址与公网地址一对一转换
NAPT实现私网地址与公网地址的多对一转换，而Easy IP适用于出接口地址无法预知的场合
NAT Server使公网主机可以主动连接私网服务器获取服务
对FTP等上层应用需要作ALG处理
本章总结

## Slide 23
谢谢大家